## Slide 1: Computer Organization
CS345
David Monismith
Based upon notes by Dr. Bill Siever and notes from the Patterson and Hennessy Text

## Slide 2: Overview
Last time: Coverage of floating point instructions
This time: Review of floating point instructions Coverage of MIPS memory and the Program Counter

## Slide 3: Program Counter
Recall that computers use a stored program model
Instructions and data are stored in memory
The next instruction to run is selected and stored in the program counter
This instruction is fetched from memory, decoded, and executed
The Program Counter (PC) is a special register that determines which instruction to run next.
The PC is incremented by 4 after fetching the next instruction to run.
It is not possible to directly modify the value within the PC, but it can be modified indirectly.

## Slide 4: Program Counter
Branches, jumps, and returns indirectly change the value of the PC since they move to a different location in the instruction memory.
From a hardware (HW) perspective, the PC provides the first portion of the fetch, decode, execute cycle.
The PC provides the address of the next instruction to fetch from memory. This instruction is fetched and then decoded by the Control Unit.
The Control Unit signals the executable components of the CPU including the ALU and Registers, and data memory access.

## Slide 5: Assembler memory usage
The "green sheet" at the front of the textbook shows how memory is allocated in the MIPS processor.
Memory is segmented or broken into parts with specific uses
0x0 to 0x00400000 is reserved for use by the Operating System
Note that instructions for input, output, terminating a program, sound, etc., are provided by the operating system, not the CPU.
0x00400000 to 0x10000000 is reserved for instructions - that is, the .text section of your program.
This leaves enough room for 66,060,028 instructions. Many constants may exist here, too.

## Slide 6: Assembler memory usage
0x10000000 to 0x10008000 is the static data section, which is used for data that must exist for the entire runtime of a program such as globals, initialization data for arrays, predefined strings, etc.
0x10008000 onwards - dynamic data segment - grows downward in memory.
  This is also referred to as the heap or free storage.
  Data allocated with new or malloc is stored here.
  This area in memory is used to store dynamically allocated memory.
0xfffffffc up to 0x10008000 - the stack - grows upward in memory toward the free store.
  Data local to each function/subroutine/method is stored here.
  This includes local variables.

## Slide 7: Next Class
Next time we'll continue to discuss memory and we will start to look at functions.