## Slide 1
Memory Management: Caching
Operating Systems
CS550

## Slide 2: CPU Caching
Cache is on chip memory used by the CPU to decrease the average time to access memory
Modern CPUs have 3 types of cache, in general.
  Data cache - variables are stored here
  Instruction cache - operations to run are stored here
  Translation look aside buffer - used to speed up virtual to physical memory access for both instructions and data
Cache hit - processor immediately reads data from or writes to cache
Cache miss - cache allocates a new entry reading in data from memory
Cache lines - representation of a block of memory in cache

## Slide 3: Cache entry structure
tag - identifier for the cache line and part of the memory address
data block - data for the cache line
flag bits - valid and dirty bits
  valid - indicates whether block has been loaded with valid data
  dirty - indicates whether block has been changed since it was read from memory. Dirty means we need to save it to main memory.
Replacement Policies
Same as regular memory replacement policies
Least Recently Used
First In First Out
Optimal
TAG | DATA BLOCK | FLAG BITS

## Slide 4: Associative Cache
Used to decide where in cache a memory entry will go.
See http://upload.wikimedia.org/wikipedia/commons/9/93/Cache%2Cassociative-fill-both.png
Fully associative - replacement policy may choose any entry
Set association - memory entries are mapped to specific locations in cache
Important in programming for high performance systems, because interleaving data in loops may allow for fewer cache misses

## Slide 5: Translation Lookaside Buffer (TLB)
memory management hardware for cache
improves speed to translate virtual addresses
includes basic memory information such as references to pages, frames, and variables.

## Slide 6: Memory Access
Uniform memory access
Memory location accessed is independent of the processor
Non-uniform memory access (NUMA)
Systems where memory access times vary wildly
Memory location accessed depends upon the processor

## Slide 7: Cache Coherency
Consistency of data on cache shared by local resources (CPUs). Three levels of coherence
  Write ops appear to occur instantly
  Processors see the same changes of values for each operand
  Different processors might see an op and assume different values (non-coherence)
Implemented by
  Snooping - individual caches monitor other caches
  Snarfing - cache controller watches addresses and memory and updates its data copies once other data is updated in memory
  Concurrency protocol - how to implement coherence
Ccnuma
  allows for consistent memory image across sockets
  IPC used to keep a consistent memory image when more than one cache stores the same memory location

## Slide 8: Thrashing
Virtual memory is constantly switching memory between cache and memory and between memory and disk
Constant paging
Resolve by
  Increasing RAM
  Rewriting programs
  Reducing memory usage
  Increasing spatial locality
Spatial locality can be increased by using proper looping

## Slide 9: Looping
Improper
int arr[1000][1000];
for(i = 0; i < 1000; i++)
{
for(j = 0; j < 1000; j++)
arr[j][i] = getValue();
}
Proper
int arr[1000][1000];
for(i = 0; i < 1000; i++)
{
for(j = 0; j < 1000; j++)
arr[i][j] = getValue();
}